## Slide 1: Smart Irrigation System
A soil moisture sensor, and a water pump to automate
the process of watering plants
(17-03-2023)
Priyanshu Gupta
200014045037
BCA 3rd Year
Annu Shukla
200013139026
Btech(CSE) 3rd Year

## Slide 2: INTRODUCTION
The Smart Irrigation System automates plant watering using a Raspberry Pi, a soil moisture sensor, and a water pump. It solves the problem of time-consuming and suboptimal manual watering by continuously measuring soil moisture and adjusting water flow accordingly. The result is healthier plants and saved time.
The Smart Irrigation System solves the problem of inefficient and inconsistent manual watering of plants. Manual watering can be time-consuming and lead to under- or over-watering, affecting plant health. The system automates plant watering using a soil moisture sensor and water pump, ensuring optimal moisture levels for healthy plant growth without manual intervention.

## Slide 3: PROJECT OVERVIEW
The Smart Irrigation System project uses a combination of hardware and software components to automate the process of watering plants. Here's an overview of the key components:
Raspberry Pi: A credit card-sized computer that runs the software needed to control the system. The Raspberry Pi is connected to the soil moisture sensor and the water pump and acts as the brain of the system.
Soil Moisture Sensor: A sensor that measures the moisture level of the soil. The sensor is inserted into the soil near the plant and sends a signal to the Raspberry Pi, which uses this information to determine whether the plant needs to be watered.
Water Pump: A pump that delivers water to the plant when it needs to be watered. The pump is controlled by the Raspberry Pi, which turns it on or off based on the readings from the soil moisture sensor.

## Slide 4: How it works?
The components of the Smart Irrigation System work together to automate the process of watering plants in the following way:
The soil moisture sensor continuously measures the moisture level of the soil around the plant.
The Raspberry Pi reads the data from the soil moisture sensor and determines whether the soil is dry enough to require watering.
If the soil is dry, the Raspberry Pi sends a signal to the water pump to turn it on and start delivering water to the plant.
The water pump delivers water to the plant until the soil moisture sensor indicates that the soil is sufficiently moist.
Once the soil reaches the desired moisture level, the Raspberry Pi sends a signal to the water pump to turn it off and stop delivering water to the plant.
This process repeats on a regular basis, ensuring that plants receive the optimal amount of water for their growth and health, without the need for manual intervention.

## Slide 5: In this diagram, the Raspberry Pi is connected to both the soil moisture sensor and the water pump through its GPIO (General Purpose Input/Output) pins. The soil moisture sensor provides an analog output that is read by one of the GPIO pins on the Raspberry Pi, while another GPIO pin is used to send a control signal to the water pump. The power supply for the water pump is also connected separately to ensure that it has sufficient power to operate.
Raspberry Pi
GPIO Pins
Soil Moisture Sensor
Analog Output
Water Pump
Power Supply Control Signal
Figure:
Diagram showing the connection between the Raspberry Pi, soil moisture sensor, and water pump:
HARDWARE SETUP

## Slide 6: Brief explanation of each connection
Raspberry Pi GPIO pins: The GPIO pins on the Raspberry Pi are used to connect it to other hardware components in the system. In this case, one GPIO pin is used to read the analog output from the soil moisture sensor, while another GPIO pin is used to send a control signal to the water pump.
Soil moisture sensor analog output: The soil moisture sensor provides an analog output signal that is proportional to the moisture level in the soil. This signal is connected to one of the Raspberry Pi's GPIO pins, which can read the voltage level and convert it into a digital value that can be processed by the software.
Water pump power supply: The water pump requires a separate power supply to operate, which is connected to a power source (such as a battery or AC outlet) and then to the pump itself. This ensures that the pump has sufficient power to operate and can deliver water to the plants effectively.
Water pump control signal: The Raspberry Pi sends a control signal to the water pump via another GPIO pin. This signal tells the pump when to turn on or off based on the moisture level in the soil. When the soil is dry, the Raspberry Pi sends a signal to turn the pump on and deliver water to the plants. When the soil is sufficiently moist, the Raspberry Pi sends a signal to turn the pump off and stop delivering water.

## Slide 7: SOFTWARE SETUP
To install gpiozero on your system, you can follow these steps:
Open a terminal or command prompt on your system.
Check if you have pip installed by running the command:
pip --version
If you see output with version information, then pip is already installed. Otherwise, you can download and install pip by following the instructions on the official pip website.
Install the gpiozero library by running the command:
pip install gpiozero
This will download and install the library and its dependencies.
Verify that the installation was successful by running a Python interpreter and importing the library:
python
python >>> import gpiozero
If you don't see any error messages, then the library was successfully installed and you can proceed to use it in your Python code.
Steps to install required Python library(gpiozero)

## Slide 8: Steps to clone or download the project repository
To clone or download the project repository, these steps were followed:
Open the project's GitHub repository in your web browser.
Click on the green "Code" button.
If Git is already installed on computer, click on "Open with GitHub Desktop" or "Download ZIP". If not, click on "Download ZIP".
If you clicked on "Open with GitHub Desktop", choose a directory to clone the repository to and click "Clone".
If you clicked on "Download ZIP", extract the contents of the ZIP file to a directory of your choice.

## Slide 9: RESULTS
The project is able to successfully automate the process of watering plants based on soil moisture levels. The Raspberry Pi reads the soil moisture sensor and turns the water pump on or off accordingly. The command prompt also provides an interface for manual control of the water pump. The project has been set up correctly and is able to maintain optimal soil moisture levels for healthy plant growth.

## Slide 10: Conclusion and future improvements
In conclusion, the project successfully automated the process of watering plants using a Raspberry Pi, soil moisture sensor, and water pump. With the help of the command prompt , users can monitor the soil moisture level and control the water pump manually.
As for future improvements, here are a few suggestions:
Using a more accurate sensor to measure the soil moisture level.
Adding more sensors to monitor other environmental factors like temperature and humidity.
Implementing a scheduling feature that automatically waters the plants at specific intervals.
Implementing a notification system to alert users when the soil moisture level is too low or too high.
Using machine learning algorithms to optimize the watering process based on the plant species and environmental factors.

## Slide 11: REFERENCES
The official websites for the Raspberry Pi (https://www.raspberrypi.org/) and Python (https://www.python.org/)
The documentation for the gpiozero library (https://gpiozero.readthedocs.io/)
Online forums and communities such as the Raspberry Pi forum (https://www.raspberrypi.org/forums/)
Python subreddit (https://www.reddit.com/r/Python/) to find information and ask questions related to the project